## Slide 1: OLSRv2 Simulation for MANET
Final presentation

## Slide 2: Agenda
Optimized Link State Routing Protocol Ver. 2
Project description
The Simulator
Protocol Analysis & Observations
Questions & Open Discussion

## Slide 3: Optimized Link Status Protocol
Based on 1-hop & 2-hop Neighbors sets
Neighborhood knowledge is achieved using NHDP (Hello messages HB)
Multi Point Relay set

## Slide 4: Optimized Link Status Protocol
MPR
  Each node notifies its MPR set for their nomination (Using TC message flooding)
  MPRs broadcast their new role
All nodes can now build a routing table
Source
Target
MPR
MPR
MPR
MPR
MPR

## Slide 5: Project Description
Project scope
  Simulating MANET environment implementing OLSRv2 protocol
  Event driven simulator
  Dynamic topology
  Topology layouts
    Uniform
    clusters
  MPR selection
  Fully configurable (protocol, world parameters)

## Slide 6: Protocol Analysis
Chart: Minimal MPR Selection, Data through All, Uniform topology
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064
Static | 0.0092 | 0.0159 | 0.0231 | 0.0286 | 0.0359 | 0.0317
Slow | 0.0075 | 0.0113 | 0.0187 | 0.0209 | 0.0296 | 0.0297
Medium | 0.0065 | 0.0117 | 0.0177 | 0.0201 | 0.0268 | 0.0268
Fast | 0.0054 | 0.0106 | 0.0166 | 0.0189 | 0.0232 | 0.0245
Chart: Maximal MPR Selection, Data method unimportant, Uniform topology
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064
Static | 0.0075 | 0.0114 | 0.0174 | 0.0195 | 0.0243 | 0.0265
Slow | 0.0059 | 0.009 | 0.0133 | 0.0155 | 0.0125 | 0.0187
Medium | 0.0047 | 0.0077 | 0.0102 | 0.0112 | 0.0161 | 0.0164
Fast | 0.0037 | 0.0063 | 0.0111 | 0.0122 | 0.0145 | 0.0152
Minimal MPR selection is has 25% better utility then selecting all neighbors as MPRs
500x500 world size, 30 stations,
reception radius 100, Hello intervals 30
TC intervals 90

## Slide 7: Protocol Analysis Cont.
Chart: Minimal MPR Selection, Data through MPR only, Uniform topology
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064
Static | 0.0073 | 0.0175 | 0.0234 | 0.0236 | 0.0297 | 0.0319
Slow | 0.0062 | 0.0112 | 0.0168 | 0.0216 | 0.0224 | 0.0253
Medium | 0.0049 | 0.0104 | 0.0137 | 0.0182 | 0.0198 | 0.0231
Fast | 0.0051 | 0.0089 | 0.0118 | 0.0168 | 0.0174 | 0.0199
Chart: Minimal MPR Selection, Data through All, Cluster topology
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064
Static | 0.0102 | 0.0166 | 0.0316 | 0.032 | 0.0338 | 0.0205
Slow | 0.0092 | 0.0154 | 0.0217 | 0.0251 | 0.0382 | 0.0248
Medium | 0.0089 | 0.0158 | 0.0292 | 0.0288 | 0.0293 | 0.0191
Fast | 0.0069 | 0.0139 | 0.0218 | 0.0294 | 0.0213 | 0.0125
500x500 world size, 30 stations,
reception radius 100, Hello intervals 30
TC intervals 90
Sending data packets through MPRs does not improve the utilization. (Even lowers it slightly)
Cluster topology has drastic effect on utilization, especially with higher data packet rates

## Slide 8: Protocol Analysis Cont.
Chart: Maximal MPR Selection, Data method unimportant, Cluster topology
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064
Static | 0.0075 | 0.0107 | 0.0133 | 0.0202 | 0.0245 | 0.0269
Slow | 0.0053 | 0.009 | 0.0126 | 0.0145 | 0.0145 | 0.0204
Medium | 0.0051 | 0.0104 | 0.0107 | 0.0146 | 0.0181 | 0.0167
Fast | 0.0046 | 0.0091 | 0.0117 | 0.0155 | 0.0207 | 0.0167
Chart: Minimal MPR Selection, Data through MPR only, Cluster topology
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064
Static | 0.009 | 0.0232 | 0.0272 | 0.0353 | 0.0426 | 0.0391
Slow | 0.006 | 0.0145 | 0.0189 | 0.0285 | 0.0273 | 0.0306
Medium | 0.0071 | 0.0163 | 0.0207 | 0.0194 | 0.0345 | 0.0369
Fast | 0.0076 | 0.0208 | 0.0235 | 0.0246 | 0.0308 | 0.0206
Cluster topology utilization is much lower as expected due to “bottleneck” phenomenon. Selecting a larger MPR set actually helps in these topology layouts.
500x500 world size, 30 stations,
reception radius 100, Hello intervals 30
TC intervals 90

## Slide 9: Protocol Analysis Cont.
Chart: Optimal settings
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Static | 0.0186 | 0.0269 | 0.0361 | 0.0461 | 0.0435 | 0.0446 | 0.0458 | 0.05
Slow | 0.0126 | 0.0181 | 0.0219 | 0.0231 | 0.0243 | 0.0255 | 0.0282 | 0.0289
Medium | 0.0112 | 0.0153 | 0.0225 | 0.0237 | 0.0249 | 0.027 | 0.026 | 0.0277
Fast | 0.0099 | 0.0166 | 0.021 | 0.0227 | 0.0212 | 0.0253 | 0.0257 | 0.0261
Setup
Static – Hello interval: 1000, TC interval: 2500
Dynamic – Hello interval: 300, TC interval: 900

## Slide 10: Protocol Architecture
GUI
Log
OLSR Nodes
Event Gen
Topology Mgr
Tasks Queue
Dispatcher
OLSRv2 Layer
(per node)
Dispatcher
Event Generator
Tasks Queue
Log
GUI
Topology Manager

## Slide 11: The Simulator
Different parameters
Simulation Time
Data Transfer Between Stations

## Slide 12: The Simulator Cont.
Uniform formation
Cluster Distribition

## Slide 13: The Simulator – Logger &SQL
Data Send & Receive
TC Msg. Send & Receive
Congestion Ctrl.

## Slide 14
Questions
&
Open Discussion

## Slide 15
Thank you !
Assaf Israel
Eli Nazarov
Asi Bross